## Slide 1
IT304 Computer Networks Week 2-Lecture 3-Layering

## Slide 2: Design Philosophy of DARPA Internet Protocols
Top level goal: effective technique for multiplexed utilization of existing interconnected networks
The Internet must… (sorted based on importance)
  continue despite loss of networks or gateways
  support multiple types of communications service
  accommodate a variety of networks
  permit distributed management of its resources
  be cost effective
  permit host attachment with a low level of effort
  resources used in the internet architecture must be accountable
Notes: state information which describes the on-going conversation must be protected.

## Slide 3: Design Philosophy of DARPA Internet Protocols
Top level goal: effective technique for multiplexed utilization of existing interconnected networks
The Internet must… (sorted based on importance)
  continue despite loss of networks or gateways
    state information which describes the on-going conversation must be protected
  support multiple types of communications service
    TCP, UDP
  accommodate a variety of networks
    including military and commercial facilities
D. Clark. 1988. The design philosophy of the DARPA internet protocols. SIGCOMM Comput. Commun. Rev. 18, 4 (August 1988),
Notes: state information which describes the on-going conversation must be protected.

## Slide 4: Protocol “layers”
Networks are complex,
with many “pieces”:
  hosts
  routers
  links of various media
  applications
  protocols
  hardware, software
Question: is there any hope of organizing structure of network?

## Slide 5: Layering of airline functionality
ticket (purchase)
baggage (check)
gates (load)
runway (takeoff)
airplane routing
departure
airport
arrival
airport
intermediate air-traffic
control centers
airplane routing
airplane routing
ticket (complain)
baggage (claim
gates (unload)
runway (land)
airplane routing
ticket
baggage
gate
takeoff/landing
airplane routing
layers: each layer implements a service
  via its own internal-layer actions
  relying on services provided by layer below

## Slide 6: Why layering?
dealing with complex systems:
explicit structure allows identification, relationship of complex system’s pieces
  layered reference model for discussion
modularization eases maintenance, updating of system
  change of implementation of layer’s service transparent to rest of system

## Slide 7: What’s a protocol?
Human protocols:
“what’s the time?”
“I have a question”
introductions
Network protocols:
computers (devices) rather than humans
all communication activity in Internet governed by protocols
Protocols define the format, order of messages sent and received among network entities, and actions taken on message transmission, receipt
Rules for:
… specific messages sent
… specific actions taken when message received, or other events

## Slide 8: What’s a protocol?
A human protocol and a computer network protocol:
Q: other human protocols?
Hi
Hi
Got the
time?
2:00
time
TCP connection
response
<file>
TCP connection
request
GET http://gaia.cs.umass.edu/kurose_ross
Notes: Explain important points
distributed entities, exchanging messages (governed by protocols)
Time going down
go over definition of protocol (showing format, order of messages sent and received, and actions taken)
We’ll see these kinds of diagrams a lot

## Slide 10
Question:
How is the structure of the Network organized?

## Slide 11
Each protocol instance talks virtually to its peer
Each layer communicates only by using the services below
Lower layer services are accessed by an interface
At bottom, messages are carried by the medium

## Slide 12: Internet protocol stack
application: supporting network applications
  FTP, SMTP, HTTP
transport: process-process data transfer
  TCP, UDP
network: routing of datagrams from source to destination
  IP, routing protocols
link: data transfer between neighboring network elements
  Ethernet (802.3), WiFi (802.11), PPP
physical: bits “on the wire”
application
transport
network
link
physical

## Slide 13
Kleinrock's "Narrow Waist" Model
Vint Cerf and Bob Kahn

## Slide 14: The Open Systems Interconnection (OSI) Reference Model by International Standards Organization (ISO)
Layers created for different abstractions
Each layer performs well-defined function
Function of layer chosen with standards in mind
Minimize information flow across layer interfaces
Find the optimum number of layers

## Slide 15
Who is the source (S) computer?
Who is the destination (D) computer?
Who is passing this message to whom?
A gift box example for encapsulating / packing message from S to D

## Slide 16: Encapsulation
source
application
transport
network
link
physical
Ht
Hn
M
segment
Ht
datagram
destination
application
transport
network
link
physical
Ht
Hn
Hl
M
Ht
Hn
M
Ht
M
M
network
link
physical
link
physical
Ht
Hn
Hl
M
Ht
Hn
M
Ht
Hn
M
Ht
Hn
Hl
M
router
switch
message
M
Ht
M
Hn
frame