## Slide 1: IT304 Computer Networks
Week6_Lec2_CDNandDASH

## Slide 2: Video Streaming and CDNs: context
stream video traffic: major consumer of Internet bandwidth
  Netflix, YouTube, Amazon Prime: 80% of residential ISP traffic (2020)
challenge: scale - how to reach ~1B users?
challenge: heterogeneity
  different users have different capabilities (e.g., wired versus mobile; bandwidth rich versus bandwidth poor)
solution: distributed, application-level infrastructure

## Slide 3: Multimedia: video
video: sequence of images displayed at constant rate
  e.g., 24 images/sec
digital image: array of pixels
  each pixel represented by bits
coding: use redundancy within and between images to decrease # bits used to encode image
  spatial (within image)
  temporal (from one image to next)
……………………..
spatial coding example: instead of sending N values of same color (all purple), send only two values: color value (purple) and number of repeated values (N)
……………….…….
frame i
frame i+1
temporal coding example: instead of sending complete frame at i+1, send only differences from frame i

## Slide 4: Multimedia: video
……………………..
spatial coding example: instead of sending N values of same color (all purple), send only two values: color value (purple) and number of repeated values (N)
……………….…….
frame i
frame i+1
temporal coding example: instead of sending complete frame at i+1, send only differences from frame i
CBR: (constant bit rate): video encoding rate fixed
VBR: (variable bit rate): video encoding rate changes as amount of spatial, temporal coding changes
examples:
  MPEG 1 (CD-ROM) 1.5 Mbps
  MPEG2 (DVD) 3-6 Mbps
  MPEG4 (often used in Internet, 64Kbps – 12 Mbps)

## Slide 5: Streaming stored video
Main challenges:
server-to-client bandwidth will vary over time, with changing network congestion levels (in house, access network, network core, video server)
packet loss, delay due to congestion will delay playout, or result in poor video quality
simple scenario:
video server
(stored video)
client
Internet

## Slide 6: Streaming stored video: challenges
continuous playout constraint: during client video playout, playout timing must match original timing
  … but network delays are variable (jitter), so will need client-side buffer to match continuous playout constraint
other challenges:
  client interactivity: pause, fast-forward, rewind, jump through video
  video packets may be lost, retransmitted

## Slide 7: Streaming multimedia: DASH
server:
  divides video file into multiple chunks
  each chunk encoded at multiple different rates
  different rate encodings stored in different files
  files replicated in various CDN nodes
  manifest file: provides URLs for different chunks
client
?
client:
  periodically estimates server-to-client bandwidth
  consulting manifest, requests one chunk at a time
    chooses maximum coding rate sustainable given current bandwidth
    can choose different coding rates at different points in time (depending on available bandwidth at time), and from different servers
...
...
...
Dynamic, Adaptive Streaming over HTTP

## Slide 8: Streaming multimedia: DASH
...
...
...
“intelligence” at client: client determines
  when to request chunk (so that buffer starvation, or overflow does not occur)
  what encoding rate to request (higher quality when more bandwidth available)
  where to request chunk (can request from URL server that is “close” to client or has high available bandwidth)
Streaming video = encoding + DASH + playout buffering
client
?

## Slide 9: Content distribution networks (CDNs)
challenge: how to stream content (selected from millions of videos) to hundreds of thousands of simultaneous users?
option 1: single, large “mega-server”
  single point of failure
  point of network congestion
  long (and possibly congested) path to distant clients
….quite simply: this solution doesn’t scale

## Slide 10: Content distribution networks (CDNs)
challenge: how to stream content (selected from millions of videos) to hundreds of thousands of simultaneous users?
  enter deep: push CDN servers deep into many access networks
    close to users
    Akamai: 240,000 servers deployed
    in > 120 countries (2015)
option 2: store/serve multiple copies of videos at multiple geographically distributed sites (CDN)
  bring home: smaller number (10’s) of larger clusters in POPs near access nets
    used by Limelight

## Slide 11: How does Netflix work?
…
…
…
…
…
…
subscriber requests content, service provider returns manifest
Netflix: stores copies of content (e.g., MADMEN) at its (worldwide) OpenConnect CDN nodes
where’s Madmen?
manifest file
  using manifest, client retrieves content at highest supportable rate
  may choose different rate or copy if network path congested
Notes: 11
Akamai: 100,000+ servers in 1000+ clusters in 1000+ networks in 70+ countries serving trillions of requests a day.
How many people use Netflix?

## Slide 12: Content distribution networks (CDNs)
…
…
…
…
…
…
Internet host-host communication as a service
OTT challenges: coping with a congested Internet from the “edge”
  what content to place in which CDN node?
  from which CDN node to retrieve content? At which rate?
OTT: “over the top”
Notes: 12
peak load: 7million viewers, 2 Tbytes via

## Slide 13: CDN content access: a closer look
netcinema.com
KingCDN.com
1
1. Bob gets URL for video http://netcinema.com/6Y7B23V
from netcinema.com web page
2
2. resolve http://netcinema.com/6Y7B23V
via Bob’s local DNS
netcinema’s
authoratative DNS
3
3. netcinema’s DNS returns CNAME for
http://KingCDN.com/NetC6y&B23V
4
5
6. request video from
KINGCDN server,
streamed via HTTP
KingCDN
authoritative DNS
Bob’s
local DNS
server
Bob (client) requests video http://netcinema.com/6Y7B23V
video stored in CDN at http://KingCDN.com/NetC6y&B23V
Notes: This slide retired, since there’s the Netflix example which is visually better