## Slide 1: IT 305 Computer Networks Week7 – Lec1
TCP Congestion Control

## Slide 2: Principles of congestion control
Congestion:
informally: “too many sources sending too much data too fast for network to handle”
manifestations:
  long delays (queueing in router buffers)
  packet loss (buffer overflow at routers)
different from flow control!
congestion control: too many senders, sending too fast
flow control: one sender too fast for one receiver

## Slide 3: Causes/costs of congestion: scenario 1
Simplest scenario:
maximum per-connection throughput: R/2
Host A
Host B
throughput: lout
large delays as arrival rate approaches capacity
Q: What happens as arrival rate lin approaches R/2?
original data: lin
R
two flows
one router, infinite buffers
input, output link capacity: R
infinite shared output link buffers
R
no retransmissions needed
R/2
delay
lin
R/2
R/2
R/2
lout
lin
throughput:
lin

## Slide 4: Causes/costs of congestion: scenario 2
one router, finite buffers
Host A
Host B
lin : original data
l'in: original data, plus retransmitted data
finite shared output link buffers
sender retransmits lost, timed-out packet
  application-layer input = application-layer output: lin = lout
  transport-layer input includes retransmissions : l’in lin
lout
R
R

## Slide 5: Causes/costs of congestion: scenario 2
Host A
Host B
lin : original data
l'in: original data, plus retransmitted data
finite shared output link buffers
R
R
copy
timeout
Realistic scenario: un-needed duplicates
packets can be lost, dropped at router due to full buffers – requiring retransmissions
but sender times can time out prematurely, sending two copies, both of which are delivered
free buffer space!
when sending at R/2, some packets are retransmissions, including needed and un-needed duplicates, that are delivered!
“wasted” capacity due to un-needed retransmissions
lin
R/2
lout
throughput:
R/2

## Slide 6: Causes/costs of congestion: scenario 2
“costs” of congestion:
more work (retransmission) for given receiver throughput
unneeded retransmissions: link carries multiple copies of a packet
  decreasing maximum achievable throughput
Realistic scenario: un-needed duplicates
packets can be lost, dropped at router due to full buffers – requiring retransmissions
but sender times can time out prematurely, sending two copies, both of which are delivered
when sending at R/2, some packets are retransmissions, including needed and un-needed duplicates, that are delivered!
“wasted” capacity due to un-needed retransmissions
lin
R/2
lout
throughput:
R/2

## Slide 7: Causes/costs of congestion: insights
upstream transmission capacity / buffering wasted for packets lost downstream
delay increases as capacity approached
un-needed duplicates further decreases effective throughput
loss/retransmission decreases effective throughput
throughput can never exceed capacity

## Slide 8: Approaches towards congestion control
End-end congestion control:
no explicit feedback from network
congestion inferred from observed loss, delay
data
data
ACKs
ACKs
approach taken by TCP

## Slide 9: TCP congestion control: AIMD
approach: senders can increase sending rate until packet loss (congestion) occurs, then decrease sending rate on loss event
AIMD sawtooth
behavior: probing
for bandwidth
TCP sender Sending rate
time
  increase sending rate by 1 maximum segment size every RTT until loss detected
Additive Increase
  cut sending rate in half at each loss event
Multiplicative Decrease

## Slide 10: TCP AIMD: more
Multiplicative decrease detail: sending rate is
Cut in half on loss detected by triple duplicate ACK (TCP Reno)
Cut to 1 MSS (maximum segment size) when loss detected by timeout (TCP Tahoe)
Why AIMD?
AIMD – a distributed, asynchronous algorithm – has been shown to:
  optimize congested flow rates network wide!
  have desirable stability properties

## Slide 11: TCP congestion control: details
TCP sender limits transmission:
cwnd is dynamically adjusted in response to observed network congestion (implementing TCP congestion control)
LastByteSent- LastByteAcked
<
cwnd
last byte
ACKed
last byte sent
cwnd
sender sequence number space
available but not used
TCP sending behavior:
roughly: send cwnd bytes, wait RTT for ACKS, then send more bytes
TCP rate
~
~
cwnd
RTT
bytes/sec
sent, but not-yet ACKed
(“in-flight”)

## Slide 12: TCP slow start
when connection begins, increase rate exponentially until first loss event:
  initially cwnd = 1 MSS
  double cwnd every RTT
  done by incrementing cwnd for every ACK received
Host A
one segment
Host B
RTT
time
two segments
four segments
summary: initial rate is slow, but ramps up exponentially fast

## Slide 13: TCP: from slow start to congestion avoidance
Q: when should the exponential increase switch to linear?
A: when cwnd gets to 1/2 of its value before timeout.
Implementation:
variable ssthresh
on loss event, ssthresh is set to 1/2 of cwnd just before loss event
* Check out the online interactive exercises for more examples: http://gaia.cs.umass.edu/kurose_ross/interactive/
X