## Slide 1: IT304 Computer Networks Week8-Lec2
Network layer Fundamentals

## Slide 2: Two key network-layer functions
network-layer functions:
forwarding: move packets from a router’s input link to appropriate router output link
routing: determine route taken by packets from source to destination
  routing algorithms

## Slide 3: IP Protocol

## Slide 4: IP addressing: introduction
IP address: 32-bit identifier associated with each host or router interface
interface: connection between host/router and physical link
  router’s typically have multiple interfaces
  host typically has one or two interfaces (e.g., wired Ethernet, wireless 802.11)
223.1.1.1
223.1.1.2
223.1.1.3
223.1.1.4
223.1.2.9
223.1.2.2
223.1.2.1
223.1.3.2
223.1.3.1
223.1.3.27
223.1.1.1 = 11011111 00000001 00000001 00000001
223
1
1
1
dotted-decimal IP address notation:

## Slide 5
Example Of Dotted Decimal
Notation
A 32-bit number in binary
10000000 00001010 00000010 00000011
The same
notation
32-bit
number expressed in
dotted
decimal
128 . 10 . 2 . 3

## Slide 6: What comprises an IP address?
Set of decimal numbers
192.168.123.132
What can we understand from this?
  NOTHING
How do routers interpret this decimal number?
  Set of binary digits
  1100000010101000111101110000100
  Can we make sense of it now?
Break the bunch of bits into 4 parts (8 bits each)
  11000000. 10101000.01111011.10000100
  Subnet Mask: local or remote network?
  11000000.10101000.01111011.10000100
  11111111. 11111111. 11111111. 00000000
  -------------------------------------------------------
11000000. 10101000. 01111011.00000000
------------------------------------------------------
  Network part: 192.168.123.0 (all 1s in the mask)
  Host part:0.0.0.132 (all 0s in the mask)

## Slide 7: What is an IP address?

## Slide 8
How does a router move packets from a it’s input link to an appropriate

## Slide 9: Destination-based forwarding
Notes: Text for this animation:
This all works out pretty nice and looks pretty simple!
But of course the devil is in the details, as the saying goes.
What happens, for example, when a subset of addresses say in this first range should go to say interface 3, rather than interface 0. Well, of course we could split the first address range into multiple pieces, and add in this new subrange with its new destination output port. But it turns out there’s a much simpler and elegant way to do this. Known as longest prefix matching.

## Slide 10: Longest prefix matching
when looking for forwarding table entry for given destination address, use longest address prefix that matches destination address.
longest prefix match
Destination Address Range
11001000 00010111 00010
11001000 00010111 00011000
11001000 00010111 00011
otherwise
Link interface
0
1
2
3
********
***
********
***
********
11001000 00010111 00011000 10101010
examples:
which interface?
which interface?
11001000 00010111 00010110 10100001

## Slide 11: Longest prefix matching
Destination Address Range
11001000 00010111 00010
11001000 00010111 00011000
11001000 00010111 00011
otherwise
Link interface
0
1
2
3
11001000 00010111 00011000 10101010
examples:
which interface?
which interface?
********
***
********
***
********
11001000 00010111 00010110 10100001
match!

## Slide 12: Longest prefix matching
Destination Address Range
11001000 00010111 00010
11001000 00010111 00011000
11001000 00010111 00011
otherwise
Link interface
0
1
2
3
11001000 00010111 00011000 10101010
examples:
which interface?
which interface?
********
***
********
***
********
11001000 00010111 00010110 10100001
match!

## Slide 13: Longest prefix matching
Destination Address Range
11001000 00010111 00010
11001000 00010111 00011000
11001000 00010111 00011
otherwise
Link interface
0
1
2
3
11001000 00010111 00011000 10101010
examples:
which interface?
which interface?
********
***
********
***
********
11001000 00010111 00010110 10100001
match!

## Slide 14: Classes in IP addresses
Number of networks
Number of hosts
Class
Lowest Address
Highest Address
A
B
C
D
E
1.0.0.0
128.1.0.0
192.0.1.0
224.0.0.0
240.0.0.0
126.0.0.0
191.255.0.0
223.255.255.0
239.255.255.255
255.255.255.254

## Slide 15: Subnets
223.1.1.1
223.1.1.2
223.1.1.3
223.1.1.4
223.1.2.9
223.1.2.2
223.1.2.1
223.1.3.2
223.1.3.1
223.1.3.27
What’s a subnet ?
  device interfaces that can physically reach each other without passing through an intervening router
network consisting of 3 subnets
IP addresses have structure:
  subnet part: devices in same subnet have common high order bits
  host part: remaining low order bits

## Slide 16: Subnets
223.1.1.1
223.1.1.2
223.1.1.3
223.1.1.4
223.1.2.9
223.1.2.2
223.1.2.1
223.1.3.2
223.1.3.1
223.1.3.27
Recipe for defining subnets:
detach each interface from its host or router, creating “islands” of isolated networks
each isolated network is called a subnet
subnet mask: /24
(high-order 24 bits: subnet part of IP address)
subnet
223.1.3.0/24
subnet 223.1.1.0/24
subnet 223.1.2.0/24

## Slide 17: Subnets
where are the subnets?
what are the /24 subnet addresses?
223.1.1.1
223.1.1.3
223.1.1.4
223.1.2.2
223.1.2.6
223.1.3.2
223.1.3.1
223.1.3.27
223.1.1.2
223.1.7.0
223.1.7.1
223.1.8.0
223.1.8.1
223.1.9.1
223.1.9.2
223.1.2.1
subnet 223.1.1/24
subnet 223.1.7/24
subnet 223.1.3/24
subnet 223.1.2/24
subnet 223.1.9/24
subnet 223.1.8/24