## Slide 1: IT305 Computer Networks
Wireless Networks Intro-I

## Slide 2: Radio Wave Propagation
Radio channels are extremely random, and are not easily analyzed
Modeling the radio channel is typically done in statistical fashion
https://www.vcelink.com/blogs/focus/difference-between-wired-and-wireless-network
[1]
[1]

## Slide 3: Wireless link characteristics: fading (attenuation)
  Wireless radio signal attenuates (loses power) as it propagates (free space “path loss”)
Free space path loss ~ (fd)2
f: frequency
d: distance
higher frequency or longer distance
larger free space
path loss
Notes: Wikipedia figure

## Slide 4: Linear Path Loss
Suppose s(t) of power Pt is transmitted through a given channel
The received signal r(t) of power Pr is averaged over any random variations due to shadowing.
We define the linear path loss of the channel as the ratio of transmit power to receiver power
We define the path loss of the channel also in dB

## Slide 5: Line-of-Sight Propagation
Attenuation
  The strength of a signal falls off with distance
Free Space Propagation
  The transmitter and receiver – CLEAR line of sight (LOS) path between them. No other sources of impairment!
  Satellite systems and microwave systems undergo free space propagation
  The free space power received by an antenna which is separated from a radiating antenna by a distance is given by Friis free space equation

## Slide 6: Friis Free Space Equation
The relation between the transmit and receive power is given by Friis free space equations:
 2
(4 d )2
Pr  Pt Gt Gr
Pt
P
r
Gt and Gr are the transmit andt receive antenna gains
 is the wavelength
d is the T-R separation
Pt is the transmitted power
Pr is the received power
Pt and Pr are in same units
Gt and Gr are dimensionless quantities.
Gr

## Slide 7: Basic Propagation Mechanisms
Reflection, diffraction, and scattering:
Reflection occurs when a propagating electromagnetic wave impinges upon an object
Diffraction occurs when the radio path between the transmitter and receiver is obstructed by a surface that has sharp edges
Scattering occurs when the medium through which the wave travels
  consists of objects with dimensions that are small compared to the wavelength, or
  the number of obstacles per unit volume is large.
Scattering
Transmitter
Receiver
Diffraction

## Slide 8: Wireless link characteristics: multipath
  multipath propagation: radio signal reflects off objects ground, built environment, arriving at destination at slightly different times
line of sight
(LOS) path
reflected path
reflected path

## Slide 9: Wireless link characteristics: multipath
  multipath propagation: radio signal reflects off objects ground, built environment, arriving at destination at slightly different times
Tc: coherence time
Coherence time:
amount of time bit is present in channel to be received
influences maximum possible transmission rate, since coherence times can not overlap
inversely proportional to
  frequency
  receiver velocity
transmitted
pulses
received
pulse
received
LOS pulse
received
multipath
pulses
time
time
received
LOS pulse
received
multipath
pulses

## Slide 10: Wireless link characteristics: noise
interference from other sources on wireless network frequencies: motors, appliances
SNR: signal-to-noise ratio
  larger SNR – easier to extract signal from noise (a “good thing”)
SNR versus BER tradeoff
  given physical layer: increase power -> increase SNR->decrease BER
  SNR may change with mobility: dynamically adapt physical layer (modulation technique, rate)

## Slide 11: Wireless link characteristics: hidden terminals
A
B
C
Hidden terminal problem
B, A hear each other
B, C hear each other
A, C can not hear each other means A, C unaware of their interference at B
A
B
C
A’s signal
strength
space
C’s signal
strength
Attenuation also causes “hidden terminals”
B, A hear each other
B, C hear each other
A, C can not hear each other interfering at B

## Slide 12: Elements of a wireless network
wired network
infrastructure

## Slide 13: Elements of a wireless network
wired network
infrastructure
wireless hosts
laptop, smartphone, IoT
run applications
may be stationary (non-mobile) or mobile
  wireless does not always mean mobility!

## Slide 14: Elements of a wireless network
wired network
infrastructure
base station
typically connected to wired network
relay - responsible for sending packets between wired network and wireless host(s) in its “area”
  e.g., cell towers, 802.11 access points

## Slide 15: Elements of a wireless network
wired network
infrastructure
wireless link
typically used to connect mobile(s) to base station, also used as backbone link
multiple access protocol coordinates link access
various transmission rates and distances, frequency bands

## Slide 16: Characteristics of selected wireless links
Indoor
Outdoor
Midrange
outdoor
Long range
outdoor
10-30m
50-200m
200m-4Km
4Km-15Km
2 Mbps
4G LTE
802.11ac
802.11n
802.11g
802.11b
3.5 Gbps
600 Mbps
54 Mbps
11 Mbps
Bluetooth
802.11ax
14 Gbps
5G
10 Gbps
802.11 af,ah

## Slide 17: Elements of a wireless network
wired network
infrastructure
infrastructure mode
base station connects mobiles into wired network
handoff: mobile changes base station providing connection into wired network

## Slide 18: Elements of a wireless network
ad hoc mode
no base stations
nodes can only transmit to other nodes within link coverage
nodes organize themselves into a network: route among themselves

## Slide 19: Wireless network taxonomy
single hop
multiple hops
infrastructure
(e.g., APs)
no
infrastructure
host connects to base station (WiFi, cellular) which connects to larger Internet
no base station, no connection to larger Internet (Bluetooth, ad hoc nets)
host may have to relay through several wireless nodes to connect to larger
Internet: mesh net
no base station, no connection to larger Internet. May have to relay to reach other a given wireless node MANET, VANET

## Slide 20: Wired Vs Wireless